## Slide 1
Torch Lake Water Quality Trends
and the National Lakes Assessment
Dennis McCauley and Michelle VandenBrand
Great Lakes Environmental Center, Inc., Traverse City, MI

## Slide 2
Torch Lake
18,770 acres (7,596 hectares),
Max. depth of 87 meters (288 feet),
Average depth of 111 feet,
Michigan’s deepest inland lake,
41 miles of shoreline,
Approximately 2 miles wide (3.2 Km) at its widest point.
Michigan’s second largest lake; second to Houghton Lake (20,044 acres).

## Slide 3: TORCH LAKE WATER QUALITY TRENDS
DATA SOURCES
  1990-2017
  Antrim County Conservation District
  Cooperative Lake Monitoring Data
  2017 National Lakes Assessment
Water Transparency
Chlorophyll @
Total Phosphorus
Temperature

## Slide 4
Parameter | Location | Minimum value (date recorded) | Maximum value (date recorded) | Average | Number of data points
Total Phosphorus (µg/L) | Torch Lake, North | 1.5 (12 events) | 14 (September 2004) | 3.3 | 23
 | Torch Lake, South | 1.5 (13 Events) | (2004) | 3.5 | 26
Secchi Disk Depth (feet) | Torch Lake, North | 12 (September 2004) | 45 (June 2007) | 27 | 323
 | Torch Lake, South | 11 (September 1995) | 52 (June 2017) | 25 | 356
Chlorophyll a (µg/L) | Torch Lake, North | 0.12 (June 1996) | 1.20 (July 1990) | 0.45 | 105
 | Torch Lake, South | 0.05 (July 1995) | 1.40 (June 1990) | 0.43 | 128
Water Temperature (°C) | Torch Lake, North | 11.7 (June 2003) | 21.6 (August 2003) | 17.7 | 12
 | Torch Lake, South | 16.0 (June 2003) | 28.3 (June 2001) | 21.5 | 22
Air Temperature (°C) | Torch Lake, North | 14.4 (September 1997) | 26.7 (September 1996) | 23.0 | 23
 | Torch Lake, South | 15.6 (June 1994) | 31.1 (August 1995) | 21.6 | 59
SUMMARY OF WATER QUALITY PARAMETERS FOR THE NORTH AND SOUTH BASINS OF TORCH LAKE: 1976-2017

## Slide 5
Chart: Secchi Disk Depth Yearly Averages
| 1976 | 1977 | 1978 | 1979 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
Torch Lake, North | 27.6667 | 23.1875 | 20.1667 | 27.4615 | 26.1818 | 22.4545 | 23.5714 | 24.3333 | 23.5385 | 23.7 | 23 | 24.4118 | 25.4687 | 27.4211 | 29.1579 | 27.5556 | 28.1579 | 25.6071 | 30.0556 | 28.6053 | 27.9286 | 27.6333 | 29.4 | 30.38
Torch Lake, South | 16.8727 | 30.8333 | 31.7143 | 22.5833 | 23.3182 | 24.4286 | 26.25 | 22.1429 | 23 | 18.7917 | 24.5833 | 25 | 22.0385 | 20.3333 | 19.25 | 21.125 | 20.8182 | 21.1818 | 23 | 31.8571 | 22 | 26.7333 | 28.2941 | 28.625 | 25.7143 | 27.5 | 25.7692 | 23.8214 | 27.4118 | 34.5833 | 36.5556

## Slide 6
Chart: Seasonal Variation in Secchi Disk Depth for Torch Lake, North
| 38122 | 38134 | 38144 | 38151 | 38159 | 38166 | 38177 | 38181 | 38193 | 38204 | 38211 | 38223 | 38229 | 38234 | 38242 | 38248 | 38256
Secchi (ft) | 40 | 36 | 35 | 30 | 30 | 30 | 30 | 30 | 25 | 16 | 16 | 18 | 15 | 19 | 17 | 12 | 16
Secchi (ft) | 31 | 30.5 | 31 | 31 | 30.5 | 33 | 34 | 41 | 20.5 | 19 | 14 | 15 | 18 | 17 | 21 | 21
Secchi (ft) | 31 | 40.5 | 40 | 32 | 36 | 33.5 | 33 | 30 | 28.5 | 33 | 25.5 | 19.5 | 21.5 | 18.5 | 19 | 21 | 21.5 | 19.5 | 17.5
Secchi (ft) | 43.5 | 34 | 23 | 41.5 | 39.5 | 44.5 | 42.5 | 39.5 | 34.5 | 25.5 | 24.5 | 22 | 19 | 20.5 | 20.5 | 21.5 | 21.5 | 20 | 16.5
Secchi (ft) | 42 | 41 | 38 | 34 | 35 | 36.5 | 30.5 | 26 | 21.5 | 16 | 22.5 | 24.5 | 21.5 | 20 | 18 | 24 | 22.5 | 22.5
Secchi (ft) | 41.5 | 34.5 | 38.5 | 35 | 38 | 38.5 | 27.5 | 35 | 36 | 29 | 26 | 21 | 14.5 | 19 | 16 | 19.5 | 22 | 21.5 | 22
Secchi (ft) | 38 | 35 | 34 | 32 | 32 | 29 | 23.5 | 21 | 20.5 | 19 | 21 | 14.5 | 19 | 20
Secchi (ft) | 41 | 38 | 38 | 38 | 38 | 35 | 35 | 35 | 32 | 30 | 31 | 29 | 26 | 21 | 19 | 18 | 18 | 19
Secchi (ft) | 38 | 35 | 34 | 38 | 35 | 38 | 36 | 28 | 36 | 35 | 29 | 26 | 21 | 14 | 19 | 16 | 22 | 21.5 | 22
Secchi (ft) | 43 | 31.5 | 31.5 | 32.5 | 32.5 | 28.5 | 31 | 33.5 | 24.5 | 20 | 19.5 | 17 | 20.5 | 25.5
Secchi (ft) | 29.5 | 29.5 | 31 | 34.5 | 32.5 | 29.5 | 34.5 | 30.5 | 31 | 25.5 | 25 | 22 | 18.5 | 21 | 20
Secchi (ft) | 39.5 | 39.5 | 38 | 38.5 | 36.5 | 35 | 32 | 29.5 | 25 | 25.5 | 21.5 | 19.5 | 20 | 22 | 19

## Slide 7
Chart: Seasonal Variation in Secchi Disk Depth for Torch Lake, South
| 38142 | 38146 | 38156 | 38164 | 38169 | 38175 | 38182 | 38189 | 38195 | 38226 | 38232 | 38234 | 38238 | 38242 | 38253 | 38253
Secchi (ft) | 36 | 26 | 32 | 26 | 26 | 28 | 31 | 24 | 21 | 18 | 17 | 16 | 17 | 16.5 | 17 | 16.5
Secchi (ft) | 33 | 33 | 33 | 33 | 35 | 32 | 32 | 32 | 32 | 32 | 32 | 32 | 28 | 27
Secchi (ft) | 25 | 21 | 19 | 23
Secchi (ft) | 38 | 32 | 31 | 42 | 37.5 | 36.5 | 22 | 18 | 13 | 23 | 22.5 | 22 | 20.5 | 21 | 22
Secchi (ft) | 36 | 39 | 45 | 34 | 35 | 34 | 30 | 25 | 25 | 20 | 17 | 19 | 19 | 22 | 29 | 29 | 23
Secchi (ft) | 46 | 45 | 39 | 40 | 31 | 36 | 34 | 25 | 24 | 23 | 23 | 22 | 20 | 18 | 15 | 17
Secchi (ft) | 30 | 42 | 33 | 35 | 25 | 27 | 21 | 24 | 21 | 20 | 19 | 22 | 21 | 20
Secchi (ft) | 33 | 31 | 26 | 36 | 32 | 31 | 31 | 32 | 27 | 31 | 30 | 23 | 21 | 20 | 19 | 17
Secchi (ft) | 33 | 40 | 28 | 30 | 25 | 20 | 23 | 26 | 18 | 22 | 22 | 21 | 27
Secchi (ft) | 31 | 25 | 24 | 32 | 29 | 30 | 22 | 20 | 20 | 13 | 24 | 20 | 19.5 | 24
Secchi (ft) | 27 | 29 | 35 | 37 | 36 | 33 | 36 | 35 | 30 | 26 | 21 | 21 | 16 | 18 | 24 | 22 | 20
Secchi (ft) | 50 | 33 | 40 | 44 | 48 | 46 | 36 | 31 | 26 | 21 | 22 | 18

## Slide 8
Chart: Secchi Disk Depth Box Plot
| Torch Lake, North | Torch Lake, South
 | 12 | 11
 | 8 | 8
 | 5.5 | 5
 | 8.25 | 7
 | 10.75 | 21

## Slide 9
Chart: Chlorophyll a Yearly Averages
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
Torch Lake, North | 0.83333 | 0.28571 | 0.29833 | 0.35 | 0.404 | 0.43667 | 0.395 | 0.28667 | 0.44 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.4575
Torch Lake, South | 0.73333 | 0.18333 | 0.3 | 0.25429 | 0.27333 | 0.35167 | 0.304 | 0.36125 | 0.50714 | 0.45 | 0.355 | 0.42167 | 0.394 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5

## Slide 10
Chart: Chlorophyll a Box Plot
| Torch Lake, North | Torch Lake, South
 | 0.12 | 0.05
 | 0.18 | 0.24
 | 0.08 | 0.1
 | 0.1 | 0.0875
 | 0.72 | 0.9225
BOX PLOT OF CHLOROPHYLL @ DATA FOR THE NORTH AND SOUTH BASINS OF TORCH LAKE: 1990-2003

## Slide 11
Chart: Total Phosphorus Yearly Averages
| 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
Torch Lake, North - Spring | 1 | 6 | 5 | 1 | 5 | 3 | 10 | 1.5 | 1.5 | 2.5 | 1.5 | 1.5
Torch Lake, North - Summer | 14 | 4 | 2 | 3 | 3 | 1.5 | 6 | 1.5 | 2.5 | 2.5 | 1.5 | 0.925
Torch Lake, South - Spring | 13 | 6 | 4 | 2 | 5 | 2 | 7 | 1.5 | 1.5 | 2.5 | 1.5 | 1.5
Torch Lake, South - Summer | 10 | 6 | 1 | 5 | 3 | 2 | 8 | 1.5 | 3 | 1.5 | 2.5 | 2.5 | 1.5 | 1.5
TOTAL PHOSHORUS DATA FOR THE NORTH AND SOUTH BASINS OF TORCH LAKE: 1990-2017

## Slide 12: SEASONAL VARIATION IN TOTAL PHOSPHORUS CONCENTRATION FOR THE NORTH BASIN OF TORCH LAKE: 2004-2017
Chart: Total Phosphorus in Torch Lake, North
| 38107 | 38235 | 38470 | 38597 | 38835 | 38963 | 39200 | 39326 | 39936 | 40300 | 40663 | 40787 | 41149 | 41399 | 41518 | 41777 | 41890 | 42130 | 42254 | 42508 | 42617 | 42872 | 42981
Torch Lake, North | 1.5 | 14 | 6 | 2.5 | 5 | 1.5 | 1.5 | 1.5 | 5 | 1.5 | 10 | 1.5 | 6 | 1.5 | 1.5 | 1.5 | 2.5 | 2.5 | 2.5 | 1.5 | 1.5 | 1.5 | 1.5

## Slide 13: SEASONAL VARIATION IN TOTAL PHOSPHORUS CONCENTRATION FOR THE SOUTH BASIN OF TORCH LAKE: 2004-2017
Chart: Total Phosphorus in Torch Lake, South
| 38110 | 38235 | 38470 | 38600 | 38835 | 38960 | 39200 | 39324 | 39690 | 39936 | 40061 | 40300 | 40426 | 40663 | 40787 | 41153 | 41399 | 41517 | 41777 | 41890 | 42130 | 42249 | 42509 | 42616 | 42865 | 42981
Torch Lake, South | 13 | 10 | 6 | 6 | 2.5 | 1.5 | 1.5 | 5 | 1.5 | 5 | 1.5 | 1.5 | 8 | 7 | 1.5 | 1.5 | 1.5 | 1.5 | 1.5 | 2.5 | 2.5 | 2.5 | 1.5 | 1.5 | 1.5 | 1.5

## Slide 14: Future Monitoring
Standardized data collection
Field and Laboratory Quality Control
Choose the parameters for long-term trend monitoring
Ice Cover

## Slide 15
Torch Lake 2017
National Lakes Assessment
The Watershed Center – Grand Traverse Bay
Funding Partners:
Dole Family Foundation
Three Lakes Association
Torch Conservation Center
Torch Lake Protection Alliance

## Slide 16: 2017 National Lakes Assessment

## Slide 17
Torch Lake “X” Point
44.960000N and -85.29362W

## Slide 22
 | TP (ug/L) | TN (ug/L) | Cl (ueq/L) | SO4 (ueq/L) | Turbidity (NTU) | Hii-NonAg10 | Hii-Ag11 | Assessment (Ag/Res/Ind)12
WMT 1 | >30@ | >400 | >100# | >200 | >3 | >0.6 | >0 | > 5/5/5
XER 2 | >100 | >1000 | >500 | >1000 | >5 | >1.5 | >0.2 | > 5/5/5
NPL 3 | >150 | >2000 | >1000 | --- | >5 | >1.5 | >0.5 | > 10/6/6
SPL4 | >150* | >2000* | >1000 | --- | >5 | >1.5 | >0.5 | > 10/6/6
TPL5 | >120 | >2000 | >1000 | >5000 | >5.5 | >1.7 | >0.15 | > 9/9/9
UMW6 | >40 | >1200 | >200 | >200 | >5 | >0.6 | >0 | > 5/5/5
CPL7 | >50 | >1200 | >1000 | >400 | >5 | >1.0 | >0 | > 6/10/6
SAP8 | >35 | >800 | >125 | >300 | >5 | >0.9 | >0 | > 6/6/6
NAP9 | >30 | >600 | >100# | >300 | >5 | >0.6 | >0 | > 6/6/6
Least-disturbed Reference Screening Filter Thresholds for NLA 2012
(Upper Midwest Ecoregion is labeled as UMW )
1 WMT = Western Mountains; 2 XER = western Xeric, 3 NPL = Northern Plains, 4 SPL = Southern Plains, 5 TPL = Temperate Plains, 6 UMW = Upper Midwest, 7 Central Plains, 8 Southern Appalachians, 9 NAP = Northern Appalachians, 10 Lakeshore Physical Habitat disturbances; non-agricultural,
11 Lakeshore Physical Habitat disturbances; agricultural, 12 Sum of agricultural/residential/industrial human disturbances

## Slide 25
NLA Indicators |  | Torch Lake Results
Sample Type | Analyses | 
Water chemistry | pH | 8.24
nutrients | TOTAL PHOSPHORUS | <0.0007
nutrients | TKN | 0.458 mg/L
 | Chlorophyll a | 0.00033 mg/L
Bacteria | E.coli | <1 (MPN)
Bacteria | Total Coliforms | 5.2 (MPN)
Algal Toxin | Microcystin | 0.001 µg/L
Sediment | Total Organic Carbon | 3.8%
Sediment | grain size | Clay: 26.1%, Sand: 35.0%, Silt: 29.1%
Sediment | Chlorinated Pesticides | <1 ng/dry gram (<mdl)
Sediment | Total PCBs | <1 ng/dry gram (<mdl)
Sediment | Total PAHs | 14.0 ng/dry gram
Sediment | Percent Solids | 73.8%
Sediment | Metals (µg/L) : Aluminum | 3249/3640
 | Antimony | 0/0
 | Arsenic | 4.16/4.12
 | Cadmium | 0/0
 | Chromium | 5.9/6.2
 | Copper | 5.9/7.6
 | Iron | 5665/5667
 | Lead | 1.7/1.7
 | Manganese | 179/178
 | Mercury | 0.0053/0.0046
 | Nickel | 3.4/3.4
 | Selenium | 0.091/0.112
 | Silver | 0/0
 | Tin | 0.45/0.52
 | Vanadium | 10.7/10.9
 | Zinc | 8.2
Triazine Pesticides (water) | Atrazine Screen | 0 µg/L
Water and Sediment Quality Analysis: Torch Lake 2017

## Slide 26
Chart: Dissolved Oxygen and Temperature Profile of Torch Lake July 5, 2017
| 20.8 | 20.8 | 20.5 | 20.399999999999999 | 20.100000000000001 | 19.899999999999999 | 19.8 | 19.7 | 19.399999999999999 | 19 | 17.899999999999999 | 16.399999999999999 | 15.4 | 12.1 | 11.8 | 11 | 10.3 | 9.9 | 9.8000000000000007 | 9.7000000000000011 | 9.5 | 9 | 8.4 | 7.9 | 7.3 | 6.2 | 6.1 | 6.1 | 6 | 5.8 | 5.5 | 5.3 | 5.0999999999999996
Temperature Profile | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 22 | 24 | 26 | 28 | 30 | 32 | 34 | 36 | 38 | 40 | 42 | 43.5
Dissolved Oxygen Profile | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 22 | 24 | 26 | 28 | 30 | 32 | 34 | 36 | 38 | 40 | 42 | 43.5

## Slide 27
Lake | Trophic Status | DO1 | Chl.2 @ | Draw- down | LitCvr3 | LitRipCvr4 | RDIS5 | RVeg.6 | Total Phosphorus (mg/L) | Sechi Depth (m)
Torch | Oligotrophic | High | Good (0.00033) | small | Poor (2.91) | Poor (1.5) | Poor (0.427) | Poor (0.11) | <0.0007 | 11.5
Clear | Oligotrophic | High | Good | Med. | Poor (0.071) | Poor (0.305) | Fair (0.487) | Poor (0.447) | 21 | 8.8
Glenn | Oligotrophic | High | Good | Small | Poor 0.217) | Poor (0.424) | Poor (0.753) | Fair (0.560) | 23 | --
Comparison of Selected Water Quality and Physical Habitat Indices (Rating Over Index Value) From Two Northern Michigan Lakes and Torch Lake
1 Dissolved Oxygen, 2 Chlorophyll @, 3 Littoral Cover, 4 Avg. Littoral and Riparian Cover, 5 Anthropogenic Disturbance, 6 Riparian Cover Complexity

## Slide 28
 | TP (ug/L) | TN (ug/L) | Cl (ueq/L) | SO4 (ueq/L) | Turbidity (NTU)
UMW | >40 | >1200 | >200 | >200 | >5
Torch | <7 | 458 |  |  | >5
Comparison of the Least Disturbed Condition in the Upper Midwest EcoRegion to Torch Lake (2017)

## Slide 30
“Given these indicators and similar scoring, Torch Lake would also likely rank in the “Good” category nationally.”

## Slide 31: QUESTIONS ?